| Menu(-) |
| --- |
|  | Main Menu | Menu level 2 | Menu level 3 | Menu level4 | Remark |
| 1 | SETUP | DMX Address | 1-512 |  | Default: 1 |
|  |  | Ethernet Interface | Custom IP Address | 2.198.159.207 |  |
|  |  |  | Custom IP Mask | 255.0.0.0 |  |
|  |  |  | Universe | 000-255 | Default: 0 |
|  |  |  | Start Channel | 1-512 | Default: 1 |
|  |  |  | Ethernet to DMX | No | Default: No |
|  |  |  |  | Yes |  |
| 2 | OPTION | Pan / Tilt | Invert Pan | Off | Default: On |
|  |  |  |  | On |  |
|  |  |  | Invert Tilt | Off | Default: Off |
|  |  |  |  | On |  |
|  |  |  | Swap Pan-Tilt | Off | Default: Off |
|  |  |  |  | On |  |
|  |  |  | Encoder Pan-Tilt | Off | Default: On |
|  |  |  |  | On |  |
|  |  |  | P/T Homing Mode | Standard | Default: Standard |
|  |  |  |  | Sequenced |  |
|  |  |  | Pan Home Def Pos | 0 degree | Default: 270 degree |
|  |  |  |  | 90 degrees |  |
|  |  |  |  | 180 degrees |  |
|  |  |  |  | 270 degrees |  |
|  |  |  | Tilt Home Def Pos | 0 % | Default: 50% |
|  |  |  |  | 12.5 % |  |
|  |  |  |  | 25 % |  |
|  |  |  |  | 50 % |  |
|  |  |  |  | 75 % |  |
|  |  |  |  | 87.5 % |  |
|  |  |  |  | 100 % |  |
|  |  | Color | Color Mixing | RGB | Default: CMY |
|  |  |  |  | CMY |  |
|  |  |  | Fix Wheel Shortcut | Off | Default: On |
|  |  |  |  | On |  |
|  |  | CMY Speed | Normal |  | Default: Fast |
|  |  |  | Fast |  |  |
|  |  | Dimmer Curve | Dimmer Curve 1 |  | Default: Dimmer Curve 1 |
|  |  |  | Dimmer Curve 2 |  |  |
|  |  |  | Dimmer Curve 3 |  |  |
|  |  |  | Dimmer Curve 4 |  |  |
|  |  | Display | Off |  | Default: Off |
|  |  |  | On |  |  |
|  |  | Fan Mode | 1200W Constant |  | Default: 1200W Auto |
|  |  |  | 1200W Auto |  |  |
|  |  |  | 1000W Constant |  |  |
|  |  |  | 1000W Auto |  |  |
|  |  |  | 800W Constant |  |  |
|  |  |  | 800W Auto |  |  |
|  |  |  | 600W Constant |  |  |
|  |  |  | 600W Hold |  |  |
|  |  |  | 400W Constant |  |  |
|  |  |  | 400W Hold |  |  |
|  |  |  | Theatre |  |  |
|  |  | Setting | Default Preset | Reset To Default | Are you sure ? Yes / No |  |
|  |  |  |  | Go Back |  |  |
|  |  |  | User Preset 1 | Load preset 1 | Are you sure ? Yes / No |  |
|  |  |  |  | Save to preset 1 |  |  |
|  |  |  | User Preset 2 | Load preset 2 | Are you sure ? Yes / No |  |
|  |  |  |  | Save to preset 2 |  |  |
|  |  |  | User Preset 3 | Load preset 3 | Are you sure ? Yes / No |  |
|  |  |  |  | Save to preset 3 |  |  |
| 3 | INFORMATION | System Errors |  |  |  |  |
|  |  | Fixture Hours | Total Hours |  |  |  |
|  |  |  | Partial Hours | Reset |  |  |
|  |  |  |  | Go Back |  |  |
|  |  | Led Hours | Total Hours |  |  |  |
|  |  |  | Partial Hours | Reset |  |  |
|  |  |  |  | Go Back |  |  |
|  |  | System Version | DISP:V1.0 NET:V1.0 CTR1-XY:V1.0 CTR2-MOTOR:V1.0 CTR3-MOTOR:V1.0 CTR4-MOTOR:V1.0 |  |  |  |
|  |  | DMX Monitor |  |  |  |  |
|  |  | Fans Monitor | Base Fan 100% |  |  |  |
|  |  |  | Led Fan 100% |  |  |  |
|  |  | Network parameters | IP Address | 2.198.159.207 |  |  |
|  |  |  | IP Mask | 255.0.0.0 |  |  |
|  |  |  | MAC Address | 54-10-EC-5B-B2-32 |  |  |
|  |  | UID | 43501AB***** |  |  |  |
| 4 | MANUAL CONTROL | Reset | NO |  |  |  |
|  |  |  | Yes |  |  |  |
|  |  | Channel | 1.Cyan | 000-255 |  |  |
|  |  |  | 2.Magenta | 000-255 |  |  |
|  |  |  | 3.Yellow | 000-255 |  |  |
|  |  |  | 4.CTO | 000-255 |  |  |
|  |  |  | 5.Color Function | 000-255 |  |  |
|  |  |  | 6.Color Wheel | 000-255 |  |  |
|  |  |  | 7.Strobe | 000-255 |  |  |
|  |  |  | 8.Dimmer | 000-255 |  |  |
|  |  |  | 9.Dimmer Fine | 000-255 |  |  |
|  |  |  | 10.Iris | 000-255 |  |  |
|  |  |  | 11.Fixed Gobo | 000-255 |  |  |
|  |  |  | 12.Rotating Gobo | 000-255 |  |  |
|  |  |  | 13.Gobo Rotation | 000-255 |  |  |
|  |  |  | 14.Gobo Fine | 000-255 |  |  |
|  |  |  | 15.Prism Insertion | 000-255 |  |  |
|  |  |  | 16.Prism Rotation | 000-255 |  |  |
|  |  |  | 17.Effect Insertion | 000-255 |  |  |
|  |  |  | 18.Effect Rotation | 000-255 |  |  |
|  |  |  | 19.Frost1 | 000-255 |  |  |
|  |  |  | 20.Frost2 | 000-255 |  |  |
|  |  |  | 21.Focus | 000-255 |  |  |
|  |  |  | 22.Zoom | 000-255 |  |  |
|  |  |  | 23.Fr.shutter1 Move. | 000-255 |  |  |
|  |  |  | 24.Fr.shutter1 Swiv. | 000-255 |  |  |
|  |  |  | 25.Fr.shutter2 Move. | 000-255 |  |  |
|  |  |  | 26.Fr.shutter2 Swiv. | 000-255 |  |  |
|  |  |  | 27.Fr.shutter3 Move. | 000-255 |  |  |
|  |  |  | 28.Fr.shutter3 Swiv. | 000-255 |  |  |
|  |  |  | 29.Fr.shutter4 Move. | 000-255 |  |  |
|  |  |  | 30.Fr.shutter4 Swiv. | 000-255 |  |  |
|  |  |  | 31.Shutters Rot. | 000-255 |  |  |
|  |  |  | 32.Shutters Macro | 000-255 |  |  |
|  |  |  | 33.Shutters Macro.Sp | 000-255 |  |  |
|  |  |  | 34.Pan | 000-255 |  |  |
|  |  |  | 35.Pan Fine | 000-255 |  |  |
|  |  |  | 36.Tilt | 000-255 |  |  |
|  |  |  | 37.Tilt Fine | 000-255 |  |  |
|  |  |  | 38.Reset | 000-255 |  |  |
|  |  |  | 39.Function | 000-255 |  |  |
| 5 | TEST | Pan/Tilt |  |  |  |  |
|  |  | Colour |  |  |  |  |
|  |  | Beam |  |  |  |  |
|  |  | Gobo |  |  |  |  |
|  |  | Shutter |  |  |  |  |
|  |  | All |  |  |  |  |
| 6 | ADVANCED | Access Code xxxx | Upload Firmware | Are you sure ? Yes / No |  |  |
|  |  |  | Calibration | Pan Offset | 000-255 |  |
|  |  |  |  | Tilt Offset | 000-255 |  |
|  |  |  |  | Color Offset | 000-255 |  |
|  |  |  |  | Cyan Offset | 000-255 |  |
|  |  |  |  | Magenta Offset | 000-255 |  |
|  |  |  |  | Yellow Offset | 000-255 |  |
|  |  |  |  | CTO Offset | 000-255 |  |
|  |  |  |  | Gobo2 Offset | 000-255 |  |
|  |  |  |  | Gobo1 Offset | 000-255 |  |
|  |  |  |  | RGobo1 Offset | 000-255 |  |
|  |  |  |  | Prism Offset | 000-255 |  |
|  |  |  |  | RPrism Offset | 000-255 |  |
|  |  |  |  | Effect Offset | 000-255 |  |
|  |  |  |  | Focus Offset | 000-255 |  |
|  |  |  |  | Zoom Offset | 000-255 |  |
|  |  |  |  | Frost1 Offset | 000-255 |  |
|  |  |  |  | Frost2 Offset | 000-255 |  |
|  |  |  |  | Iris Offset | 000-255 |  |
|  |  |  |  | Shutters Rot. Offset | 000-255 |  |
|  |  |  |  | Shutter 1 M1 Offset | 000-255 |  |
|  |  |  |  | Shutter 1 M2 Offset | 000-255 |  |
|  |  |  |  | Shutter 2 M1 Offset | 000-255 |  |
|  |  |  |  | Shutter 2 M2 Offset | 000-255 |  |
|  |  |  |  | Shutter 3 M1 Offset | 000-255 |  |
|  |  |  |  | Shutter 3 M2 Offset | 000-255 |  |
|  |  |  |  | Shutter 4 M1 Offset | 000-255 |  |
|  |  |  |  | Shutter 4 M2 Offset | 000-255 |  |
|  |  |  | Menu Locking | Unlock Code XXXX |  | Default: 1234 |
|  |  |  | Recover | 60-0 s Are you sure ? Yes / No |  | 60秒倒计时，等待其他机器重新上电，超时自动退出。 |

；

| 38CH | Function | Value | Percent/Setting | Remark |
| --- | --- | --- | --- | --- |
| 1 | Cyan | 000-255 | Excluded-Inserted(CMY = On)，Inserted-Excluded(CMY = Off) |  |
| 2 | Magenta | 000-255 | Excluded-Inserted(CMY = On)，Inserted-Excluded(CMY = Off) |  |
| 3 | Yellow | 000-255 | Excluded-Inserted(CMY = On)，Inserted-Excluded(CMY = Off) |  |
| 4 | CTO | 000-255 |  |  |
| 5 | Color Function | 000-085 086-170 171-255 | Whole color Half color Linear path | Color Wheel <= 69 |
| 6 | Color Wheel | 000-009 010-019 020-029 030-039 040-049 050-059 060-069 | Open Color 1 Color 2 Color 3 Color 4 Color 5 Color 6 | Whole color |
|  |  | 000-004 005-009 010-014 015-019 020-024 025-029 030-034 035-039 040-044 045-049 050-054 055-059 060-064 065-069 | Open Open + Color1 Color 1 Color 1 + Color 2 Color 2 Color 2 + Color 3 Color 3 Color 3 + Color 4 Color 4 Color 4 + Color 5 Color 5 Color 5 + Color 6 Color 6 Color 6 + Open | Half color |
|  |  | 000-009 010-019 020-029 030-039 040-049 050-059 060-069 | Open (0,1,2,3,4,5,6,7,8,9) Color 1 (0,1,2,3,4,5,6,7,8,9) Color 2 (0,1,2,3,4,5,6,7,8,9) Color 3 (0,1,2,3,4,5,6,7,8,9) Color 4 (0,1,2,3,4,5,6,7,8,9) Color 5 (0,1,2,3,4,5,6,7,8,9) Color 6 (0,1,2,3,4,5,6,7,8,9) | Linear path |
|  |  | 070-127 | Slow to Fast(CW) | Rainbow |
|  |  | 128-255 | Positioning from 0-360 degrees(Indexing) | Indexing |
| 7 | Strobe | 000-003 004-103 104-107 108-207 208-212 213-225 226-238 239-251 252-255 | Closed Slow to Fast Strobe (1-25Hz) Open Slow to Fast Pulsation Open Random Slow Strobe Random Medium Strobe Random Fast Strobe Open |  |
| 8 | Dimmer | 000-255 | Dimmer 0%-100% |  |
| 9 | Dimmer Fine | 000-255 | Dimmer Fine |  |
| 10 | Iris | 000-127 128-131 132-171 172-211 212-251 252-255 | Minimum to Maximum Aperture Maximum Aperture Slow to Fast Pulsation Slow to Fast Pulsation,Fast Opening Slow to Fast Pulsation,Fast Closing Maximum Aperture |  |
| 11 | Fixed Gobo | 000-008 009-017 018-026 027-035 036-044 045-053 054-062 063-071 072-113 114-117 118-159 160-173 174-187 188-200 201-214 215-227 228-241 242-255 | White Gobo1 Gobo2 Gobo3 Gobo4 Gobo5 Gobo6 Gobo7 Fast to Slow(Forward Spin) Stop (Stop Rotation) Slow to Fast(Revers Spin) Gobo1 Shaking Slow to Fast Gobo2 Shaking Slow to Fast Gobo3 Shaking Slow to Fast Gobo4 Shaking Slow to Fast Gobo5 Shaking Slow to Fast Gobo6 Shaking Slow to Fast Gobo7 Shaking Slow to Fast |  |
| 12 | Rotating Gobo | 000-010 011-020 021-030 031-040 041-050 051-060 061-071 072-113 114-117 118-159 160-175 176-191 192-207 208-223 224-239 240-255 | White Gobo1 Gobo2 Gobo3 Gobo4 Gobo5 Gobo6 Fast to Slow(Forward Spin) Stop (Stop Rotation) Slow to Fast(Revers Spin) Gobo1 Shaking Slow to Fast Gobo2 Shaking Slow to Fast Gobo3 Shaking Slow to Fast Gobo4 Shaking Slow to Fast Gobo5 Shaking Slow to Fast Gobo6 Shaking Slow to Fast |  |
| 13 | Gobo Rotation | 000-127 128-190 191-192 193-255 | 0 - 540 Position Fast to Slow(Forward Spin) Stop (Stop Rotation) Slow to Fast(Revers Spin) |  |
| 14 | Gobo Fine | 000-255 |  |  |
| 15 | Prism Insertion | 000-127 128-255 | Prism Excluded Prism Inserted |  |
| 16 | Prism Rotation | 000-127 128-190 191-192 193-255 | 0 - 540 Position Fast to Slow(Forward Spin) Stop (Stop Rotation) Slow to Fast(Revers Spin) |  |
| 17 | Effect | 000-255 | Effect moves linearly into the light beam |  |
| 18 | REffect | 000-003 004-127 128-131 132-255 | Stop (Stop Rotation) Slow to Fast(Forward Spin) Stop (Stop Rotation) Slow to Fast(Revers Spin) |  |
| 19 | Frost1 | 000-255 | Frost1 0->100% |  |
| 20 | Frost2 | 000-255 | Frost1 0->100% |  |
| 21 | Focus | 000-255 | Distant-Near |  |
| 22 | Zoom | 000-255 | Wide Beam-Narrow Beam |  |
| 23 | Framing Shutter 1 movent | 000-255 | Movement from outward to inward |  |
| 24 | Framing Shutter 1 swivelling | 000-127 128 129-255 | Swivelling from -25 degrees towards 0 degrees 0 degrees Swivelling from 0 degrees to +25 degrees |  |
| 25 | Framing Shutter 2 movent | 000-255 | Movement from outward to inward |  |
| 26 | Framing Shutter 2 swivelling | 000-127 128 129-255 | Swivelling from -25 degrees towards 0 degrees 0 degrees Swivelling from 0 degrees to +25 degrees |  |
| 27 | Framing Shutter 3 movent | 000-255 | Movement from outward to inward |  |
| 28 | Framing Shutter 3 swivelling | 000-127 128 129-255 | Swivelling from -25 degrees towards 0 degrees 0 degrees Swivelling from 0 degrees to +25 degrees |  |
| 29 | Framing Shutter 4 movent | 000-255 | Movement from outward to inward |  |
| 30 | Framing Shutter 4 swivelling | 000-127 128 129-255 | Swivelling from -25 degrees towards 0 degrees 0 degrees Swivelling from 0 degrees to +25 degrees |  |
| 31 | Framing Shutters Rotation | 000-127 128 129-255 | Rotation from left to center Center Rotation from center to right |  |
| 32 | Framing Shutters Macros | 000-003 004-011 012-018 019-025 026-032 033-039 040-047 048-054 055-061 062-068 069-075 076-082 083-090 091-097 098-104 105-111 112-118 119-125 126-133 134-140 141-147 148-154 155-161 162-168 169-176 177-183 184-190 191-197 198-204 205-211 212-219 220-226 227-233 234-240 241-247 248-255 | No Function Macro 1 Macro 2 Macro 3 Macro 4 Macro 5 Macro 6 Macro 7 Macro 8 Macro 9 Macro 10 Macro 11 Macro 12 Macro 13 Macro 14 Macro 15 Macro 16 Macro 17 Macro 18 Macro 19 Macro 20 Macro 21 Macro 22 Macro 23 Macro 24 Macro 25 Macro 26 Macro 27 Macro 28 Macro 29 Macro 30 Macro 31 Macro 32 Macro 33 Macro 34 Macro 35 |  |
| 33 | Framing Shutters Macro Speed | 000-255 | Speed From Slow to Fast |  |
| 34 | Pan | 000-255 | Pan Coarse |  |
| 35 | Pan Fine | 000-255 | Pan Fine |  |
| 36 | Tilt | 000-255 | Tilt Coarse |  |
| 37 | Tilt Fine | 000-255 | Tilt Fine |  |
| 38 | Reset | 000-025 026-076 077-127 128-255 | Unused Range Effects Reset (Hold 5S) Pan/Tilt Reset (Hold 5S) Complete Reset (Hold 5S) |  |
| 39 | Function | 000-040 041-050 051-060 061-070 071-080 081-090 091-100 101-110 111-120 121-130 131-140 141-150 151-160 161-170 171-180 181-190 191-200 201-210 211-220 221-230 231-240 241-246 247-252 253-255 | No Function Dimmer curve 1(Hold 3S) (Default) Dimmer curve 2 Dimmer curve 3 Dimmer curve 4 1200W Constant (Hold 3S) 1200W Auto (Hold 3S) (Default) 1000W Constant (Hold 3S) 1000W Auto (Hold 3S) 800W Constant (Hold 3S) 800W Auto (Hold 3S) 600W Constant (Hold 3S) 600W Hold (Hold 3S) 400W Constant (Hold 3S) 400W Hold (Hold 3S) Theatre (Hold 3S) Pan/Tilt Slow Speed (Hold 3S) Pan/Tilt Medium Speed (Hold 3S) Pan/Tilt Fast Speed (Hold 3S) (Default) CMY Normal Speed (Hold 3S) CMY Fast Speed (Hold 3S)(Default) DisplayOff (Hold 3S)(Default) DisplayOn (Hold 3S) No Function |  |